## Slide 1: NDE 3.5
Incremental Steps
Toward Greater Automation in NDE

## Slide 2
Why NDE 3.5 ? A Case in Point
NDE 3.5: Slightly Better Automation
Small steps – but not half measures
Examples of NDE 3.5 systems
Agenda

## Slide 3
Hanlon’s Razor*
  Do not ascribe to malice, that which is adequately explained by incompetence.
The end results of both malice and incompetence are equally problematic for our goals in NDE.
NDE 3.5 helps to prevent both of these causes.
Why NDE 3.5 ?
*aphorism also attributed to Napoleon, David Hume, J.W von Goethe

## Slide 4
Why strive for NDE 3.5 or even NDE 4.0 ?
Why do NDE at all?
  to improve safety
  to provide assurance and confidence in quality
  to improve manufacturing quality
Prior methods are demonstrably inadequate:
  Paper records, images on local disc drives, etc.
  No database integration, no integration with manufacturing MRP / ERP
  Poor traceability, no true audit capability
NDE 3.5  NDE 4.0 helps us achieve the core goals of NDE
Why Automate NDE ?

## Slide 5
What is NDE 3.5 ?
NDE 3.0
  Digital NDE : C-Scans, image files, etc.
  Stand alone inspection systems with local storage of data
  NDE not tightly integrated within manufacturing planning and scheduling
NDE 3.5
  Existing NDE systems, slightly better integrated
  Automation the entire NDE process, not just the scanning part
NDE 4.0
  Fully automated NDE, in every conceivable way
  Tightly integrated within company and global data ecosystems
  Complete fluidity of data, and metadata from NDE systems
  Remote management of systems via Digital Twins
  Machine Learning, Big Data Analytics,

## Slide 6
Analysis
Scanning
Scanning
Analysis
Recording
Analysis
Manual
New Idea
Automated
Hand held flaw detectors
Scanning Machines with Stop on Defect
C-Scans  Image Files, PDF, etc.
Evolution of NDE Process Automation
Scanning
Recording
Analysis
Reporting
1.0
2.0
3.0
Image adapted from: W. Weber, D. Mair, D. Jansen, L. Lombardi , ’Advances in Inspection Automation’ QNDE Proceedings, 2009
Scanning
Recording
Analysis
Reporting
Calibration
Alignment
Archiving
Strip Charts, C-Scans
Scanning
Recording
Analysis
Reporting
Calibration
Alignment
Archiving
Scanning
Recording
Analysis
Reporting
Calibration
Alignment
Archiving
3.5
4.0
Manufacturing
NDE
Logistics
Life Cycle
Materials
Planning
Scanning

## Slide 7
How to Approach NDE 3.5 ?
Make better use of existing NDE systems and processes.
1. Automate your NDE Instruments –
  most now have:
    Setup files – save and recall these versus manual settings
    Remote control via TCP/IP, RS-232, etc.
    Live data streaming and recording
  Scan setups and calibrations can therefore be automated.
  Instrument status can be queried remotely.
  Data can be stored and shared
2. Integrate the machines used for scanning:
  many NDE processes are already mechanized,
  these machines stand alone from the manufacturing process
Scanning machines can be connected to the factory network

## Slide 8
How to Approach NDE 3.5 ?
3. Use the Factory Database
Modern manufacturing is database driven – why not NDE?
  read the barcode - obtain the identity of the item
  report that the item is under inspection
  setup the scan according to the item type
  embed the item identity with the scan data
  report NDE results Pass / Fail / Hold
4. Get some integration software
Modern manufacturing is software driven
  NDE Instrument software needs remote control
  Robot / Machine software needs handshaking beyond simple I/O
  An integration platform is needed to connect these sub-systems

## Slide 9
NDE 3.5 is All About Metadata
Metadata is information about your inspection data.
It describes the context of how the data was collected.
If the C-Scan is the data, the metadata is the:
  instrument and probe identity – serial numbers
  identity of the inspected component – lot and serial numbers
  last calibration date and result
  instrument settings when the data was collected
  settings for automated analysis algorithm - amplitude / size criteria
  and so on..
Metadata makes possible:
  Archiving to databases
  auditing with contextual verification
  Trending and analysis for process monitoring and control.

## Slide 10
Why NDE 3.5 ?
Preventing this:
NDE connected to factory systems admin systems.
Automated setup from database.
Automated records of process steps.
Automated data storage
Regular external audit via metadata.
Customer access to data
Recognition of NDE importance in long term company.
Ethical Management

## Slide 11
NDE 3.5 in Action – Example 1: Quality for High Performance Steel
SONIX immersion tank circa 1990’s Updated in 2017 with modern software and motion control.
All original functions remain.
New Capabilities:
High speed scanning of test coupons in batch mode.
Automated analysis and decisions
Remote management
Database for setup and reporting

## Slide 12
NDE 3.5 in Action – Example 1: Quality for High Performance Steel
Coupons are automatically scanned with high frequency UT, and automatically evaluated.
Several systems globally. All use common settings and report to a central database.
Automated Analysis Software:
Detects individual coupons.
Automated analysis by coupon.
Defect detection and tabulation
Remote management
Database for setup and reporting

## Slide 13
NDE 3.5 in Action – Example 2: High Performance Bearings
High speed automated inspection of bearings includes setup, data acquisition, analysis and decision to Accept / Reject
Inspection of Inner and Outer Rings
  High Frequency Ultrasonic
  Conventional UT
Inspection Process:
  PLC Controlled – fully automated
  ~ 30 second cycle time
  UT setup from database
  Batch and Lot numbers included within UT data files
  Trending graphs reported to factory

## Slide 14
NDE 3.5 in Action – Example 2: High Performance Bearings
Screen from automated system: Operator is not normally present. Bearing is rejected

## Slide 15
NDE 3.5 in Action – Example 2: High Performance Bearings
Screen of Geometric Gate setup.
Gate settings are saved to database for retrieval during automated mode.
Analysis:
  3D Gates - settings from database
  Analysis criteria from database
  Higher detection spec. in raceways
  Automated Accept / Reject sent to PLC
  Data saved to cloud for follow-up analysis
Raceway
Gate
Body (core)
Gate

## Slide 16
NDE 3.5 in Action – Example 3: Aerospace Metals Billet Inspection
Barcode to query factory MRP database
From factory database:
  Setup Requirements – Instruments & Scan settings
  Calibration specimen and requirements
Automated Inspection
  Calibration & Fitness for Use Reporting
  Scanning & data saving with embedded metadata
  Turned shafts: all faces scanned in one operation

## Slide 17
NDE 3.5 in Action – Example 3: Aerospace Metals Billet Inspection
Semi-Automated Analysis
  Clusters are automatically detected & tabulated
  Human Analyst: classification and judgement
Automated Reporting
  1-button upload of all assessments and data files
To factory database
  Inspection Status: Completed
  Inspection Verdict: Release / Hold for follow-up
  Inspection Data Files: C-Scans, tabulated indications,
  Inspection Results: PDF report, Excel file (indications tables)

## Slide 18
Thank You
Questions ?
www.utex.com
dseto@utex.com

## Slide 19
Extras

## Slide 20
Digital Twin
Remotely
Managed
Asset
Industry 4.0
Examples:
Commercial Aircraft and engines
Power Generation Plants
Power Generation Grid
Oil and Gas assets
Real Time Asset Management
IIoT
Data In The
Cloud
Apps
In The
Cloud
Machine
Learning
Big Data
Analytics

## Slide 21
Digital Twins
Remotely
Managed
Operation
Industry 4.0
Convergent Technologies:
*IIoT = Industrial Internet of Things
Fully Automated Machines
  Local Machine Learning
Digital Twins – Cyber-Physical Systems
Big Data Analytics
  Machine Learning (AI)
Convergence and Integration of
Digital Technologies via Networks
IIoT*
Data In The
Cloud
Apps
In The
Cloud
Machine
Learning
Big Data
Analytics
NDE
Automated
Machines