## Slide 1: Challenges of Non-Destructive Evaluation in Automotive Industry
Bita Ghaffari
Ford Research & Advanced Engineering

## Slide 2: Automotive NDE needs
Precise laboratory measurements to develop and validate novel materials and/or processes
In-plant NDE for proving out novel materials and/or processes
NDE for pilot-plant operations
In-plant NDE; varied production volumes
  Prototype or limited-run
  High-volume production
Embedded sensors for structural health monitoring

## Slide 3: Automotive scale challenges
AEROSPACE | DRIVERS | AUTOMOTIVE
10s to 1,000s | Annual volume | 1,000s to 1,000,000s
Low | Cost sensitivity | High
Slow is OK | Production pace | High
Fixed process | Manufacturing | Flexibility
Small to very large | Inspection area/volume | Small to large
Very high | Geometry/material tolerance | Medium to high
100% inspection | Quality | Process control & inspections, various frequency
FAA Regulations | Regulatory | Application-dependent

## Slide 4: Industry scale – pace & cost
Pre-pandemic annual production:
Ford: ~6M vehicles; ave. price ~$45k; 1 vehicle every ~2 min (at times 24 hr/day)
Boeing/Airbus: 400-900 comm. planes; ave. price ~$100M; 1 jet every ~15 hours
Consequences of scale, roughly:
False call that shuts down the line for 1 hour might cost >$1M in revenue.
Suspect NDE results for 1 shift quarantine >200 vehicles; potentially costing >$10M.
Financial impact of new automotive NDE process ~9200 times that for aerospace, if 100% inspection.
Automotive inspection in 1/450th the time in aerospace.
$1 automotive structural health sensor ~ same fraction of cost of vehicle as $2200 aerospace sensor.
6M / 650  9200
$100M / $45k  2200
15 hr / 2 min  450
Sources: corporate.ford.com, www.statista.com, www.forbes.com, drivingconnective.com, www.coxautoinc.com, finance.yahoo.com

## Slide 5: Cost and risk
Pre-pandemic annual production:
Ford: ~6M vehicles; ave. price ~$45k; 1 vehicle every ~2 min (at times 24 hr/day)
Boeing/Airbus: 400-900 comm. planes; ave. price ~$100M; 1 jet every ~15 hours
High production rates and volumes 
  Controlled processes & In-Station Process Control
    Periodic destructive or non-destructive quality check
  Unexpected interactions:
    Risk-averse to replacing traditional quality procedures & metrics
  Favorable business case for the NDE customer
6M / 650  9200
$100M / $45k  2200
15 hr / 2 min  450
Sources: corporate.ford.com, www.statista.com, www.forbes.com, drivingconnective.com, www.coxautoinc.com, finance.yahoo.com

## Slide 6: Historical business cases – suppliers
Plastic fuel tank vapor-barrier thickness
Destructive test: 1 tank/hr per press
  Scrap cost: ~$200k/year
  Labor/time: ~$120k/year
NDE: Ultrasound:
  Hardware: ~$10k
  Training: minimal.
  Labor/time: ~$20k/year
Savings of ~$300,000/year
Crankshaft hardness/heat treatment
Destructive test: 1 crankshaft per shift
  Scrap: ~$20k/year
  Labor/time ~$20k/year
NDE: Eddy current:
  Complicated part  trained inspector
  Fully-automated machine: ~$400k
Not cost effective.

## Slide 7
Very large Microcrack
Validate novel process & alloy: porthole hydroformed Al tube; splits along 3 seam lines, microcrack in one location
Challenges:
  Boundary split size almost invisible to naked eye
  Boundary microcrack on continuum of orange peel
  Component prove-out: large # of parts
  Large inspection area (360) in ~4 min
  Visual inspection not possible (operator fatigue)
  Very different tube cross sections (circular to trapezoidal)
  Complicated non-cylindrical tube shape
Split
High prove-out volumes
Circular cross section
Microcrack
location
Notes: 7

## Slide 8
High prove-out volumes
Challenge:
Probe failure due to large # of parts
Outcome:
Fast supplier response
~9000 tubes scanned; process & alloys successfully validated
Solution:
High-resolution, sensitive flexible Eddy current array probe
Manual inspection
Highly-customized fixture to rotate part
Automated flag of each defect
Needed to scan 1000’s of tubes
Slide direction
C-scan of tube surface
Notes: 8

## Slide 9: Challenge of customary engineering specs
1 mm
Small bridge height
Lack of adhesion
1 mm
Partial penetration
Baseline braze
Replace/reduce destructive test of laser welded & laser brazed joints (Ford & U. of Windsor)
Challenges:
Precise & discrete measurement of several imperfection types
  joint geometry, pore/crack, weld penetration, lack of adhesion, melting of base metal.
Variable joint geometry on the same component
Small joint
High surface curvature

## Slide 10: Challenge of customary engineering specs
Solution:
Ultrasonic 1D array, Full Matrix Capture & Adaptive Total Focusing Method
First- and second-order image corrections
AI-based identification of imperfections
Corrected ultrasonic image CT Scan
2 mm
Baseline braze
Lack of adhesion
Ultrasonic & CT mages, courtesy Dr. Andrew Ouellette
First-order corrections
First- & second-order corr
Simulated geometry

## Slide 11: Conclusions
DRIVERS | AUTOMOTIVE
Annual volume | 1,000s to 1,000,000s
Cost sensitivity | High
Production pace | High
Manufacturing | Flexibility
Inspection area/volume | Small to large
Geometry/material tolerance | Medium to high
Quality | Process control & inspections, various frequency
Regulatory | Application dependent
Favorable business case
  Who is ultimate customer?
  Inspector training
  Is automation or in-situ a solution?
    Flexibility required
Novel process or material vs. established
High volume demands controlled processes & In-Station Process Control (ISPC)
  Periodic quality check
Risk-averse in replacing traditional quality procedures & metrics
Thank you!